Complete Preflight

| Before Starting Engine |
| --- |
| Seats & Belts | Adjusted & Locked |
| Brakes | Test & Set |
| Fuel Selector | Both |
| Cowl Flaps | Open |

| Starting Engine |
| --- |
| Radio Master | Off |
| Mixture | Rich |
| Prop Pitch | Low (high rpm) |
| Carburetor Heat | Cold |
| Master Switch | On |
| Circuit Breakers | Check |
| Test Fuel Pump | Check |
| Primer | 2 – 5 Strokes |
| Throttle | Pump 2 1/8 Open |
| Propeller Area | Clear |
| Ignition Switch | START |
| Throttle Set | 1000 RPM |
| Engine Gages | Check |

| Before Taxi |
| --- |
| Radios Master | On |
| Com & Nav | Set |
| Transponder | Standby |
| Nav Lights/Beacon | As Needed |
| Instrument w/ATIS | Set |
| Heading Indicator/Compass | Set |
| Contact Ground | Intentions |
| Test Brakes | Check |

| Before Takeoff |
| --- |
| Point Aircraft Into Wind | Check |
| Flight Controls | Check |
| Trim Tab | Takeoff Setting |
| Throttle | 1800 RPM |
| Engine Instruments | Check |
| Cycle Prop 2 - 3 Times | Check |
| Full Carburetor Heat | Check |
| Magnetos (50 rpm Max Difference – 100 Max Drop) | Check |
| Alternator | Check |
| Manifold Pressure | Check |
| Suction Gage (4.6 – 5.4 inches) | Check |
| Return to Idle | Check |
| Flight Instruments | Set |
| Radio & Intercom | Set |
| Wing Flaps | Takeoff Setting |
| Transponder | Altitude |
| Clearing Turn | Check |
| Cabin Doors/Windows | Latched & Locked |
| Contact Tower | Intentions & Clearance |
| Note Time of Takeoff | Check |

##### HELENA FREQUENCIES

###### ATIS			 	120.40

GROUND		 	121.90

##### TOWER			118.30

# APPROACH			119.5

# UNICOM			122.95

FLIGHT SERVICE		122.55

VORTAC			117.70

| Takeoff |
| --- |
| Wing Flaps Min w/Crosswind | As Needed |
| Carburetor Heat | Cold |
| Prop Pitch | Low |
| Mixture (To Alt) | Set |
| Clearing Turn | Check |
| Note Time of Takeoff | Check |
| Radio Intentions | Check |
| Power | Full |
| Rotate | 60 mph |
| Climb Speed | 90 mph (Vy) |
| Raise Flaps Slowly | Alt & Speed |
| Adjust Trim | As Needed |
| MAX Performance Takeoff |
| Wing Flaps Min w/Crosswind | 10 Degrees |
| Carburetor Heat | Cold |
| Prop Pitch | Low |
| Mixture (To Alt) | Set |
| Clearing Turn | Check |
| Note Time of Takeoff | Check |
| Radio Intentions | Check |
| Brakes | Apply |
| Power | Full |
| Brakes | Release |
| Rotate | 60 mph |
| Climb Speed | 60 mph (Vx) |
| Raise Flaps Slowly | Alt & Speed |
| Adjust Trim | As Needed |
| Cruise Climb |
| Power | 23”MP 2450 RPM |
| Speed | 100 - 120 mph |
| Adjust Trim | As Needed |
| Select Fuel Tank | As Needed |
| Cowl Flaps Open as nec. Cruise |
| Power | MP 23in. 2450 RPM |
| Adjust Mixture | As Needed |

| Descent |
| --- |
| Carburetor Heat | On |
| Power | MP 19 in. RPM – Same |
| Adjust Trim | As Needed |
| Adjust Mixture | As Needed |
| Before Landing |
| Fuel Selector Valve | Both |
| Mixture | Rich |
| Power | Down |
| Prop | In |
| Carburetor Heat | Hot |
| Wing Flaps | As Needed |
| Airspeed – Flaps Up – Flaps Down | 80 – 90 mph 70 – 80 mph |
| Safety Belts | Secure |

| Engine Failure |
| --- |
| Airspeed (Best Glide) | 80 mph Flaps Up |
| Select Landing Area | Into Wind Turn Toward Area |
| Restart Checklist | Check/Change Fuel Tank Mixture – Rich Magnetos – Both Primer – In & Locked |
| Communicate | Declare Emergency |
| Set Up | Landing / Approach |
| Restart Fails |
| Mixture | Idle / Cut-Off |
| Fuel Valve | Off |
| Ignition | Off |
| Switches | Off (Except Master) |
| Airspeed | 70 – 80 mph (Flaps Up) |
| Wing Flaps | Extend Only When Certain Extend As Necessary |
| Airspeed | 65 – 75 mph (Flaps Down) |
| Cabin Doors | Unlatched |
| Attitude | Slightly Tail Low |
| Upon Touchdown | Apply Heavy Brake Full Up Elevator |

# Text boxes

- Shutdown –

Avionics			Off

Mixture			Full Lean

Throttle			Full In

Beacon/Lights			Off

Magnetos			Off

Master Switch			Off

##### FUEL: 	65 Gals./60 Useable